## Slide 1
GAZIRAY EMU
HV car lines

## Slide 2
HV lines
The HV architecture is visible in the image

## Slide 3
HV lines
Cables which impact on the HV 25kV line are those
highlighted, in each OA car:

## Slide 4
HV lines
Roof line layout (at the state of the design):
Cable from panto (energy meter) to HV box
Cable from HV box to disconnector
Cable from disconnector to trafo (underframe) how to consider the measures:
Cable from disconnector to jumper
The Jumper cable (spring type) is not indicated

## Slide 5
HV lines – cable 1
The first cable is the one which connects the pantograph (energy meter) to the HV box, characteristics of this cable are mainly:
Section: 95 mm2
Minimum Bending Radius: max 210 mm
Shielded, with shield termination at each extremity
Connection, panto side: straight, M12
Ground connection, panto side: straight, M10
Ground cable, lenght: 450 mm
Connection, HV box side: 90°, M12 (TBC with HVbox supplier)
Ground connection, HV box side: straight, M8
Ground cable, lenght: 450 mm
Cable Gland – included, with plate for entrance in the HV box
Measure of the cable: 3870 mm preliminary, few centimeters can change during design phase
Other Characteristics to be defined during design phase

## Slide 6
HV lines – cable 2
The 2nd cable is the one which connects the HV box to the disconnector
Section: 95 mm2
Minimum Bending Radius: max 210 mm
Shielded, with shield termination at each extremity
Connection, disconnector side: straight, M12 (TBC with Disconnector supplier)
Ground connection, disconnector side: straight, M10
Ground cable, lenght: 450 mm
Connection, HV box side: 90°, M12 (TBC with HVbox supplier)
Ground connection, HV box side: straight, M8
Ground cable, lenght: 450 mm
Cable Gland – included, with plate for entrance in the HV box
Measure of the cable: 3950 mm preliminary, few centimeters can change during design phase
Other Characteristics to be defined during design phase

## Slide 7
HV lines – cable 3
The 3rd cable is the one which connects the disconnector to the transformer (underframe), the cable shall so enter in the vehicle from an opportune hole on the roof and exit undeframe to connect the transformer; characteristics of this cable are mainly:
Section: 50 mm2
Minimum Bending Radius: max 190 mm
Shielded, with shield termination at each extremity
Connection, roof side: screw, M20, with all necessary elements (nuts, washers, …)
Ground connection, inside vehicle: straight, M10
Ground cable, lenght: 500 mm
Roof plate: TBD durign design phase
Connection, Transformer, T-connector (to be supplier separated from the cable)
Ground connection, Trafo: straight, M10
Ground cable, lenght: 300 mm
Measure of the cable: 12000 mm preliminary, few centimeters can change during design phase
Other Characteristics to be defined during design phase

## Slide 8
HV lines – cable 4
The 4th cable is the one which connects the disconnector to the spring jumper, characteristics of this cable are mainly:
Section: 95 mm2
Minimum Bending Radius: max 210 mm
Shielded, with shield termination at each extremity
Connection, disconnector side: straight, M12
Ground connection, panto side: straight, M10
Ground cable, length: 450 mm
Connection, jumper side: screw, M20, with all necessary elements (nuts, washers, …)
Ground connection, integrated in the clamp which fix the cable: M10 nut
Measure of the cable : 19900 mm preliminary, few centimeters
can change during design phase
Other Characteristics to be defined during design phase

## Slide 9
HV lines – cable 5
The 5th cable is the jumper (spring type) which connects the two OA cars
Main characteristics of the jumper will be defined during design phase, image above is only an example of a possible solution.
It will be under the scope of the supplier the definition of the main characteristics of the spring, in accordance with the circulability diagrams which will be available in design phase.